## Slide 1
CEBA CLEAN ENERGY PROCUREMENT WORKSHOP - 2026 - DAY 2 - OFFSITE SOLUTIONS DEEP-DIVE
Understanding Vietnam's DPPA Mechanisms
and Pricing Considerations
The pricing stack - the financial model - what to expect - key decision points
Virtual (grid CfD) DPPA under Decree 57/2025/ND-CP
Allotrope - 45-minute technical session + Q&A

## Slide 2
SESSION ROADMAP
Follow the money: from your EVN bill to a bankable DPPA
Understanding Vietnam's DPPA Mechanisms & Pricing - CEBA Procurement Academy 2026
2
# | Module | Min
1 | The baseline: what you pay EVN today | 4
2 | Virtual DPPA money flow: the five-line bill | 12
3 | CfD mechanics: what drives your number | 6
4 | Developer economics and the three gates | 8
5 | Case study: one factory, Cases 5 & 6 | 12
6 | Key decision points and close | 3
By the end of this session you can:
1. Decompose a virtual DPPA monthly settlement into its five components and compare it to your EVN bill
2. Explain how the CfD strike, market price (FMP), loss factors and grid fees set your net cost
3. See why buyer, seller and lender each have a gate - and why a deal must pass all three
4. Leave with realistic pricing expectations grounded in a real factory model
Assumed from this morning's session: DPPA overview, eligibility, contracting terms.
Scope: virtual (grid CfD) DPPA only.

## Slide 3
MODULE 1 - THE BASELINE (4 MIN)
What you pay EVN today: time-of-use is the reference price
Understanding Vietnam's DPPA Mechanisms & Pricing - CEBA Procurement Academy 2026
3
Period | Hours | vs base
Off-peak (thap diem) | 22:00 - 04:00 | ~0.52x
Normal (binh thuong) | 04:00-09:30, 11:30-17:00, 20:00-22:00 | 1.0x
Peak (cao diem) | 09:30-11:30, 17:00-20:00 | ~1.78x
Sunday rule: no peak period on Sundays (all hours normal).
Voltage | Off-peak | Normal | Peak (USD/kWh approx. 2025)
>=110kV | 0.034 | 0.065 | 0.116
22-110kV | 0.037 | 0.070 | 0.126
6-22kV | 0.042 | 0.079 | 0.141
<6kV | 0.049 | 0.092 | 0.164
Why this matters for DPPA
Every DPPA offer is judged against this bill - your business-as-usual (BAU)
Peak hours cost ~3.4x off-peak: your load shape decides what "average" means for you
Residual energy (load not covered by the DPPA) keeps paying these TOU rates

## Slide 4
MODULE 1 - THE BASELINE (4 MIN)
The benchmark: EVN BAU with escalation - and who can play
Understanding Vietnam's DPPA Mechanisms & Pricing - CEBA Procurement Academy 2026
4
The savings benchmark
BAU = your current EVN bill escalated ~4%/yr (historical trend 2015-2024)
A DPPA is evaluated on cumulative cost vs BAU over 10 years and over the project lifetime - not just Year 1
EVN tariff escalation is the main source of long-term DPPA value
Voltage eligibility (Decree 57/2025, Art. 16)
Voltage | K_pp (2025) | Loss rate | Virtual DPPA
>=110kV | 1.008525 | 2.79% | Eligible
22-110kV | 1.027263 | 4.56% | Eligible
6-22kV | TBD (NLDC/EVN) | - | Not yet usable
<6kV | TBD (NLDC/EVN) | - | Not yet usable
If your connection is 6-22kV or below, virtual DPPA is not yet available to you: settlement loss factors (K_pp) are still pending from NLDC/EVN.

## Slide 5
MODULE 2 - THE FIVE-LINE BILL (12 MIN)
Virtual DPPA money flow: three relationships, one bill
Understanding Vietnam's DPPA Mechanisms & Pricing - CEBA Procurement Academy 2026
5
RE GENERATOR
sells 100% of output
to the spot market
VWEM SPOT MARKET
pays generator FMP
per kWh generated
EVN
meters, wheels & bills
the DPPA customer
YOUR FACTORY
pays EVN the DPPA bill;
settles CfD with generator
energy -> market (FMP)
DPPA bill (5 lines)
CfD settlement (two-way)
Physical electrons flow through the national grid as usual - the DPPA is a financial overlay
The generator's revenue = spot sales at FMP + CfD settlement with you
Your cost = the five-line EVN bill + the CfD settlement -> next slide

## Slide 6
MODULE 2 - THE FIVE-LINE BILL (12 MIN)
Your monthly settlement has five lines
Understanding Vietnam's DPPA Mechanisms & Pricing - CEBA Procurement Academy 2026
6
# | Line | Formula | Level (2025 reference)
1 | Market energy | Q_Khc x FMP x k x K_pp | FMP avg ~1,426.6 VND/kWh; k~1.026; K_pp by voltage
2 | DPPA service fee | Q_Khc x C_dppa_dv | 360 VND/kWh
3 | Balancing fee | Q_Khc x P_cl | 163.3 VND/kWh
4 | Residual purchase | (Load - Q_Khc) x EVN retail | your TOU rates (Module 1)
5 | CfD settlement | (Strike - FMP) x min(Q_c, Q_Khc) | two-way: can be + or -
Lines 1-4 are billed by EVN. Line 5 settles bilaterally with the generator under your CfD contract.
Q_Khc = the renewable volume you actually received and consumed (defined next slide).
CFMP = FMP x k: k converts the market price to the customer delivery point (price conversion, not a volume loss).

## Slide 7
MODULE 2 - THE FIVE-LINE BILL (12 MIN)
Which volume? You settle only on what you actually consume
Understanding Vietnam's DPPA Mechanisms & Pricing - CEBA Procurement Academy 2026
7
Q_adj = Q_meter / K_pp delivered volume at your meter
Q_Khc = min(Load, Q_adj) settled volume (lines 1-3)
Q_CfD = min(Q_c, Q_Khc) CfD settles on received volume
Voltage | K_pp | Loss
>=110kV | 1.008525 | 2.79%
22-110kV | 1.027263 | 4.56%
K_pp removes grid losses: ~2.8-4.6% of plant output never reaches your meter - you do not pay for it, but you also do not receive it
If the plant generates more than you consume in an hour, the excess earns the generator spot revenue only - it is NOT billed to you and does NOT earn CfD
Practical consequence: contracted volume (Q_c) above your real consumption buys nothing

## Slide 8
MODULE 2 - WORKED EXAMPLE (NSMO, SEP-2025)
Official NSMO simulation: industrial park buys 6,000 MWh/month
Understanding Vietnam's DPPA Mechanisms & Pricing - CEBA Procurement Academy 2026
8
Parameter | Symbol | Value
Consumption = received RE volume | Q_KH = Q_Khc | 6,000,000 kWh/mo
Contracted CfD volume | Q_c | 6,000,000 kWh/mo
CfD strike price | P_c | 1,300 VND/kWh
Market price (monthly avg) | FMP | 1,200 VND/kWh
Price conversion factor | k | 1.026
Loss factor (110 kV) | K_pp | 1.008
DPPA service fee | C_dppa_dv | 360 VND/kWh
Balancing fee | P_cl | 163.3 VND/kWh
Avg retail price (residual) | P1 | 2,204 VND/kWh
Scenario
A 50 MW solar plant contracts its full output to one industrial customer
Consumption exactly equals delivered RE volume - no residual EVN purchase this month
Source: NSMO worked examples for Decree 57/2025 (Sep-2025 public training)
Strike just 100 VND above market - watch what the fees do

## Slide 9
MODULE 2 - WORKED EXAMPLE (NSMO, SEP-2025)
The five lines, computed
Understanding Vietnam's DPPA Mechanisms & Pricing - CEBA Procurement Academy 2026
9
Line | Calculation | VND/month
1 Market energy (C_DN) | 6,000,000 x 1,200 x 1.026 x 1.008 | 7,446,297,600
2 Service fee (C_dppa) | 6,000,000 x 360 | 2,160,000,000
3 Balancing fee (C_cl) | 6,000,000 x 163.3 | 979,800,000
4 Residual (C_bl) | 0 kWh x 2,204 | 0
EVN bill (C_EVN) | lines 1 + 2 + 3 + 4 | 10,586,097,600
5 CfD settlement (C_CfD) | (1,300 - 1,200) x 6,000,000 | 600,000,000
TOTAL (C_KH) | C_EVN + C_CfD | 11,186,097,600
Effective cost = 11,186,097,600 / 6,000,000 = ~1,864 VND/kWh for fully renewable supply (vs ~2,204 VND avg retail in the example)
Generator side: 6,048,000 kWh x 1,200 (spot) + 600,000,000 (CfD) = 7,857,600,000 VND

## Slide 10
MODULE 2 - THE FIVE-LINE BILL (12 MIN)
The structural cost: 523 VND/kWh of fees before any CfD
Understanding Vietnam's DPPA Mechanisms & Pricing - CEBA Procurement Academy 2026
10
Component (per matched kWh) | VND/kWh | US cents
Market energy at 2025 avg FMP x k x K_pp (22-110kV) | ~1,504 | ~6.0c
DPPA service fee (C_dppa_dv) | 360 | 1.4c
Balancing fee (P_cl) | 163.3 | 0.7c
Delivered cost before CfD | ~2,027 | ~8.1c
The 523 VND/kWh of fixed fees applies to every matched kWh, regardless of your strike
They are set by regulation, not negotiation
Compare ~2,027 VND delivered (pre-CfD) with your own TOU mix - for many factories that is already near or above average grid cost
Virtual DPPA is rarely a Day-1 discount. Its value = price certainty vs EVN escalation + credible renewable claims. Treat fee levels as the first number you check.

## Slide 11
MODULE 3 - CFD MECHANICS (6 MIN)
The CfD is two-way: certainty, not automatic savings
Understanding Vietnam's DPPA Mechanisms & Pricing - CEBA Procurement Academy 2026
11
CfD cash flow = (Strike - FMP) x Q_CfD
Market condition | Who pays whom
FMP below strike | You top up the generator
FMP above strike | Generator pays you back
Net effect: your renewable energy cost is locked near the strike (+ fees), whatever the market does
2025 reference: FMP averaged ~1,427 VND/kWh with strong hourly volatility - the CfD removes that volatility from your budget
A strike below expected average FMP would mean expected receipts - but no developer can finance that (Module 4)

## Slide 12
MODULE 3 - CFD MECHANICS (6 MIN)
Strike escalation and the Year 1 reality
Understanding Vietnam's DPPA Mechanisms & Pricing - CEBA Procurement Academy 2026
12
Strike escalation (e.g. 4%/yr)
Escalating strikes improve the seller's and lender's lifetime economics...
...but do nothing for your Year 1 cost - and compound against you later
Negotiate the escalation index as hard as the starting strike (fixed VND vs CPI vs USD-linked)
What Year 1 usually looks like
In most realistic structures, Year 1 DPPA cost is at or above BAU
Savings build as EVN tariffs escalate (~4%/yr) against your locked strike
Evaluate on 10-year and lifetime cumulative cost - never on Year 1 alone
Budget question for your CFO: can we accept a modest Year 1 premium to cap a 25-year exposure?

## Slide 13
MODULE 3 - CFD MECHANICS (6 MIN)
Contract volume vs your load shape
Understanding Vietnam's DPPA Mechanisms & Pricing - CEBA Procurement Academy 2026
13
Solar generates midday; your factory runs its own shape. The overlap - hour by hour - is all that counts.
If you... | What happens | Cost consequence
Over-contract (Q_c > consumption) | CfD caps at consumed volume - excess earns nothing | You paid contract terms for volume you can never settle
Match contract to hourly overlap | Every contracted kWh settles | Efficient - the target
Under-contract (Q_c < overlap) | More residual purchased from EVN at TOU | Less price certainty, smaller renewable claim
Ask every developer for an hourly (8760) matching analysis against YOUR meter data - not an annual percentage
Batteries can shift the overlap window but add capex the tariff must carry (see the case study)

## Slide 14
MODULE 4 - DEVELOPER ECONOMICS (8 MIN)
The other side of the table: where the developer's money comes from
Understanding Vietnam's DPPA Mechanisms & Pricing - CEBA Procurement Academy 2026
14
Revenue = Q_meter x FMP spot sales (volatile)
+ (Strike - FMP) x Q_CfD CfD with you (stabiliser)
The CfD converts volatile spot revenue into a near-fixed price on matched volume
Your strike IS the developer's bankable revenue line
Everything the lender checks flows from it
Typical Vietnam RE project finance:
70% debt / 30% equity, ~10-year debt term
Debt: ~8.5%/yr in VND - ~5%/yr in USD (international)
Equity target: 12-15%+ IRR
CIT incentives: 4 years exempt + 9 years at half rate

## Slide 15
MODULE 4 - DEVELOPER ECONOMICS (8 MIN)
A deal must pass three gates at once
Understanding Vietnam's DPPA Mechanisms & Pricing - CEBA Procurement Academy 2026
15
Gate | Who | Test | Strike pressure
BUYER | You | Cumulative cost <= BAU over 10 yr AND lifetime | pushes strike DOWN
SELLER | Developer | Equity IRR >= 12-15% | pushes strike UP
LENDER | Bank | Minimum DSCR >= ~1.20x every year | pushes strike UP (hardest gate)
DSCR = cash available for debt service / debt service, computed for every year of the loan
One bad year - e.g. a battery replacement - can sink the whole financing even if averages look fine
The negotiation window is the strike range where all three gates pass - it can be empty (case study)
A strike below the developer's bankability floor does not mean a cheap deal - it means no project.

## Slide 16
MODULE 4 - DEVELOPER ECONOMICS (8 MIN)
Lifecycle items the tariff must carry - ask about all four
Understanding Vietnam's DPPA Mechanisms & Pricing - CEBA Procurement Academy 2026
16
Item | Typical assumption | Why you should care
PV degradation | ~0.5%/yr output decline | Matched volume shrinks; lost kWh repurchased from EVN at TOU
Battery replacement | Around year 10-11, large one-off cost | Can crater DSCR in that year; ask who funds it and how
CIT holiday | 4 yr exempt + 9 yr half rate (RE projects) | Improves developer economics - value you can negotiate for
FX exposure | VND strike vs USD capex/debt | USD-linked terms shift FX risk to you; price it consciously
These rarely appear in headline term sheets, but each one moves the bankable strike floor - and therefore your price.

## Slide 17
MODULE 5 - CASE STUDY (12 MIN)
Same factory as yesterday - now going off-site
Understanding Vietnam's DPPA Mechanisms & Pricing - CEBA Procurement Academy 2026
17
Yesterday (On-Site session): Cases 1-4 explored rooftop solar + BESS behind the meter. Today: the same southern-Vietnam manufacturing facility (22-110kV) signs a virtual DPPA with a dedicated solar + storage project.
Deal frame (both cases) | Value
DPPA type | Virtual (grid CfD) under Decree 57/2025
Strike price | 2,000 VND/kWh, escalating 4%/yr
Tenor / analysis period | 25 years
Financing | 70% debt, 8.5% VND, 10-yr term
Difference between cases | Case 5: solar + LARGE battery - Case 6: solar + MINIMUM battery
Method: full 8760-hour settlement simulation (ND57 formulas, hourly FMP/CFMP series) + 25-year project cash-flow model with the three gates.

## Slide 18
MODULE 5 - CASE STUDY (12 MIN)
Case 5 - solar + large battery: the battery eats the deal
Understanding Vietnam's DPPA Mechanisms & Pricing - CEBA Procurement Academy 2026
18
Metric | Result
Seller equity IRR | 16.9%
Project IRR | 13.5%
Developer NPV | $1.52M
Minimum DSCR | 1.14x (replacement year)
Payback | 9.1 yr
Buyer vs BAU - Year 1 | -8.7%
Buyer vs BAU - 10-yr cumulative | -8.9%
Buyer vs BAU - lifetime | -9.3%
At strike 2,000 the buyer pays ~9% MORE than BAU on every horizon
The oversized battery adds a ~$1.2M replacement around year 11 that the tariff must recover
Even so, lender comfort is thin (min DSCR 1.14x < 1.20x)
Lesson 1: an oversized battery cannot carry its own replacement cost through the tariff - everyone loses.

## Slide 19
MODULE 5 - CASE STUDY (12 MIN)
Case 6 - solar + minimum battery: bankable, but the strike is the fight
Understanding Vietnam's DPPA Mechanisms & Pricing - CEBA Procurement Academy 2026
19
Metric | Result
Seller equity IRR | 26.9%
Project IRR | 18.2%
Developer NPV | $2.54M
Minimum DSCR | 1.50x (comfortably > 1.20x)
Payback | 4.7 yr
Buyer vs BAU - all horizons | -14.4%
Lean sizing: seller and lender are now comfortable - returns strong, DSCR 1.50x
But at strike 2,000 the buyer is ~14% worse than BAU: the seller's headroom IS the negotiation space
So: sweep the strike down and see where the gates cross
Lesson 2: right-sized assets make the project financeable - then the entire negotiation is the strike price.

## Slide 20
MODULE 5 - CASE STUDY (12 MIN)
Sweeping the strike on Case 6: the window is empty
Understanding Vietnam's DPPA Mechanisms & Pricing - CEBA Procurement Academy 2026
20
56 scenarios swept: strikes 1,200-2,200 VND/kWh x contract volume 70-100%. Gate results:
Strike level | Buyer gate | Seller gate | Lender gate (>=1.20x) | Balanced?
~2,000 (offer) | FAIL -14% | PASS | PASS 1.50x | No
~1,400 | FAIL -1.4% | PASS ~19% | PASS 1.19-1.5x | No
~1,300 x 70% vol | PASS +0.5% lifetime | PASS 17.9% | FAIL 1.14x | No
~1,200 | PASS +2.9% | PASS | FAIL <1.20x | No
The buyer turns positive just as the lender drops out: zero of 56 scenarios pass all three gates at current market prices and fee levels.
Pricing alone cannot balance this deal. The levers that can: lower leverage, debt sculpting, USD-denominated debt (~5%), fee relief, longer tenor - exactly this afternoon's panel.

## Slide 21
MODULE 5 - CASE STUDY (12 MIN)
What this means for your pricing expectations
Understanding Vietnam's DPPA Mechanisms & Pricing - CEBA Procurement Academy 2026
21
1. Expect low single-digit lifetime savings at best - the product you are buying is 25-year price certainty plus credible renewable claims, not a discount
2. Expect Year 1 to cost more than BAU - plan the internal approval around cumulative horizons
3. Strike offers near 2,000 VND/kWh leave the buyer deeply negative - realistic buyer-positive territory starts near ~1,300, which today fails the lender
4. Deal feasibility is decided by financing structure as much as by price - ask developers HOW their project is financed, not just what they charge

## Slide 22
MODULE 6 - DECISION POINTS (3 MIN)
Five decisions to settle before you sign
Understanding Vietnam's DPPA Mechanisms & Pricing - CEBA Procurement Academy 2026
22
# | Decision | What to check
1 | Strike level & escalation/indexation | Fixed VND vs escalating vs USD-linked; model all three vs BAU
2 | Contract volume vs load shape | 8760 hourly matching vs YOUR meter data; CfD caps at consumed volume
3 | Tenor & termination | Developer wants 15-25 yr; match to your lease / order book; exit terms
4 | Voltage eligibility & K_pp | >=22kV only today; which K_pp applies decides your loss adjustment
5 | Risk allocation | FMP volatility, curtailment, negative-CfD months, change-in-law -> this afternoon
Items 1-4 are quantifiable before negotiation - run them against your own load data first.

## Slide 23
CLOSE
Three things to remember
Understanding Vietnam's DPPA Mechanisms & Pricing - CEBA Procurement Academy 2026
23
1. Know your five-line bill - 523 VND/kWh of fees and the loss factor are fixed; the strike is the only big number you negotiate
2. Judge the deal on 10-year and lifetime cost vs BAU - never on Year 1
3. Every deal must pass buyer, seller AND lender gates - if the window is empty, the fix is structural, not just price
Next: panel discussion on risk allocation and the reality of bank financing for synthetic DPPA - bring the lender-gate question with you.

## Slide 24
BACKUP
Backup slides - Q&A reference
Understanding Vietnam's DPPA Mechanisms & Pricing - CEBA Procurement Academy 2026
24
B1 FMP market context and forward uncertainty
B2 What happens if my load drops?
B3 RECs and Scope 2 treatment of DPPA volumes
B4 6-22kV connections: current status
B5 How the buyer gate is measured

## Slide 25
BACKUP B1
FMP market context (2025)
Understanding Vietnam's DPPA Mechanisms & Pricing - CEBA Procurement Academy 2026
25
Price | VND/kWh | USD/kWh (25,000)
FMP, 2025 mean | 1,426.6 | 0.0571
CFMP, 2025 mean | 1,464.8 | 0.0586
Measured k ratio (hourly CFMP/FMP) | 1.006 - 1.060 | -
FMP is strongly seasonal and hourly-volatile; monthly averages mask large swings
Forward FMP is the single biggest uncertainty in any DPPA business case - run high/low scenarios
Figures are 2025 VWEM data - refresh before relying on them for a 2026+ decision

## Slide 26
BACKUP B2
What happens if my load drops?
Understanding Vietnam's DPPA Mechanisms & Pricing - CEBA Procurement Academy 2026
26
Settlement shrinks with you: Q_Khc = min(Load, Q_adj) - EVN lines 1-3 only ever bill consumed volume
The CfD also caps at consumed volume - but your CONTRACT may still oblige payment on contracted volume (take-or-pay style clauses)
This is a contract negotiation point, not a regulatory mechanic: check shortfall, suspension and force-majeure clauses
Match tenor and volume commitments to your realistic production outlook, not the optimistic one

## Slide 27
BACKUP B3
RECs and Scope 2 treatment
Understanding Vietnam's DPPA Mechanisms & Pricing - CEBA Procurement Academy 2026
27
DPPA volumes carry the renewable attributes you need for market-based Scope 2 accounting (see Day 1, Topic 2)
Confirm in the contract WHO owns the attributes/RECs for matched volume - and for the plant's surplus sold to market
Hourly settlement data (Q_Khc) gives you credible granular matching evidence for brand reporting

## Slide 28
BACKUP B4
6-22kV connections: current status
Understanding Vietnam's DPPA Mechanisms & Pricing - CEBA Procurement Academy 2026
28
Decree 57/2025 (Art. 16) enables virtual DPPA for >=110kV and 22-110kV connections
K_pp loss factors for 6-22kV and <6kV have not been published by NLDC/EVN - settlement cannot be computed
Practical options today: connect/upgrade to >=22kV, pursue on-site solutions (Day 1), or wait for the loss-factor announcement
Many supplier factories sit at 6-22kV - raise this with CEBA and your brand contacts as a policy ask

## Slide 29
BACKUP B5
How the buyer gate is measured
Understanding Vietnam's DPPA Mechanisms & Pricing - CEBA Procurement Academy 2026
29
Benchmark: EVN-only BAU (your current tariff escalated ~4%/yr), same load, same horizon
Gate: cumulative DPPA cost <= cumulative BAU cost over BOTH the first 10 years AND the project lifetime
Year 1 outcome is reported as context but is not the gate
A separate comparison vs an on-site alternative is useful disclosure, but the qualification test is vs BAU